## Slide 1: Inverse Design of Photonic Crystals
Using Tandem Neural Networks
MTech Thesis Presentation

## Slide 2: Introduction: The Challenge of Photonic Design
The Traditional Approach: Designing photonic structures requires slow, iterative simulations (like COMSOL).
You guess a geometry (L1, L2), run a simulation, check the bandgap, and repeat.
The Goal (Inverse Design): We want to reverse this process to input a desired bandgap and instantly output the required physical dimensions.
The Problem: Machine Learning struggles with Inverse Design because of the 'non-uniqueness' problem (different shapes producing the same bandgap).

## Slide 3: Introduction to Tandem Neural Networks
What is a Tandem Neural Network? A powerful architecture linking two separate AI models to solve inverse problems.
Model 1 (Forward Model): Acts as a fast substitute for COMSOL. Takes dimensions (L1, L2) and predicts physics (f_lower, f_upper).
Model 2 (Inverse Model): The designer. Takes a target bandgap and guesses the required L1 and L2.
How they train together: The Inverse Model makes a guess, which is fed into the frozen Forward Model to verify the bandgap match.

## Slide 4: The Dataset & Physics Extraction
Raw Data: A massive 4GB COMSOL parametric sweep containing 29.5 million rows.
The Challenge: Data contained massive spatial redundancy (710 mesh nodes duplicating frequencies).
The Physics Solution: Instantly collapsed redundant nodes and dynamically scanned the Brillouin zone (k-sweep).
Extracted the absolute bandgap edges (max of the lower band, min of the upper band).
The Result: Compressed 4GB into a pure 61-row PyTorch dataset of valid mappings.

## Slide 5: High-Fidelity Inverse Design Results
Forward Model Accuracy: Achieved an outstanding Validation Loss of ~0.007.
Tandem Model Accuracy: Achieved a Validation Loss of ~0.008.
Final Evaluation: On the 15% unseen Test Set, predicted geometries plotted almost perfectly along the y=x ground-truth line.
Conclusion: The AI successfully takes arbitrary target bandgaps and reverse-engineers highly accurate L1 and L2 parameters.

## Slide 6: What To Do Next (Future Scope)
Expand the Parameter Space: Run a much larger automated parametric sweep in COMSOL (e.g., 500-1000 geometries).
Because process_data.py is automated, retraining on larger datasets is seamless.
Add Complex Physics Targets: Expand the output to predict k-extrema locations, group velocity, or quality factors.
Physical Fabrication: Fabricate the AI's predicted structures and validate the bandgaps experimentally.